## Slide 1: Raster lidar data visualizations for interpretation of microrelief structures
dr. Žiga Kokalj
2014
Research Centre of the Slovenian Academy of Sciences and Arts (ZRC SAZU)
Centre of Excellence for Space Sciences and Technologies (Space-Si)

## Slide 2: Why different visualizations?

## Slide 3: Lidar and past cultural landscapes
forest cover in Europe is growing
  Slovenia: 39% --> 60% in the last century
DEM’s and DSM’s are mainly provided by lidar operators or national mapping authorities
they are not optimised for archaeological detection or interpretation
DTM – DSM
advanced visualisation is rarely used

## Slide 4: Visualizations
simplify interpretation of features
there is more to visualizations than shaded relief
interpretation based solely on shaded relief has a big potential to miss important archaeological features (Challis et al. 2008. Antiquity)

## Slide 5: Visualizations
1 Analytical hill-shading
2 PCA of hill-shadings
3 Colour cast
4 Trend removal
5 Slope gradient
6 Sky view factor
7 Openness
8 Solar insolation
Kokalj et al. 2011. Antiquity.
Kokalj et al. 2013. Visualizations of lidar derived relief models.

## Slide 6: Tonovcov grad
one of the largest and most important Late Antiquity settlements in the south-eastern Alps
3 early Christian churches from the 5th century
Foto: Željko Cimprič

## Slide 7
Foto: Slavko Ciglenečki

## Slide 8: Digital orthophoto
0
50 m

## Slide 9: Lidar survey
Scanning | 
scanner type | Riegl LMS-Q560
platform | helicopter
date | 4th and 16th March 2007
swath width | 60 m
flying height | 450 m
average last and only returns per m2 on a combined dataset | 11.2
Data processing | 
method | REIN (Kobler et al. 2007)
spatial resolution of the final elevation model | 0.5 m

## Slide 10: Hill-shading
the most commonly used technique (Yoëli 1965. Kartographische Nachrichten)
greyscale colour table – enhances the perception of morphology
standard: azimuth at 315°, sun elevation at 45°
surface is illuminated by a direct light
constant for the entire dataset
1

## Slide 11: Shaded relief
315° 45°
0
50 m
Lidar Data Copyright
Walks of Peace in the Soča Region Foundation

## Slide 12: Hill-shading
easy to compute and interpret
included in standard GIS software
reveals features with low light source on flat areas
dark shades and brightly lit areas
linear structures parallel to the light source

## Slide 13: Low light shading
315°
0
50 m
Lidar Data Copyright
Discovery Programme
45°
5°

## Slide 14: Illumination effects

## Slide 15: Typical ridge and furrow case study
315°
0
100 m
Lidar Data Copyright
Infoterra Global Ltd
45°
45°

## Slide 16: Hill-shading in multiple directions – RGB
RGB 0°, 337,5°, 315° 45°
0
50 m

## Slide 17: PCA of hill-shadings
summarizes information
  typically over 99% in the first three components
Devereux et al. 2008. Antiquity.
16 hill-shaded images
(100 %)
first 3 coponents
(> 99 %)
2

## Slide 18: PCA of hill-shadings - RGB
16 45°
0
50 m

## Slide 19: PCA of hill-shadings – bands 1 and 2
16 45°
0
50 m

## Slide 20: PCA of hill-shadings
removes redundancy
does not provide consistent results with different datasets

## Slide 21: Colour cast
histogram manipulation, colour ranging
limits the range of displayed values
Challis 2006. Archaeological Prospection.
3

## Slide 22: Colour cast
270 m
280 m
190 m
1220 m
0
100 m

## Slide 23: Colour cast
useful in flat terrain
retains the display of original elevation data
easy to interpret
completely fails in rugged terrain
extensive manipulation is needed

## Slide 24: Trend removal (LRM)
remove the trend in data so only small scale features remain
removes the height variation of “global” features
240 m
280 m
-5 m
5 m
4

## Slide 25: Trend removal (LRM)
several methods to assess the trend:
  averaging
  median smoothing
  Gaussian smoothing
  improvement with a “purged DEM” (Hesse. 2010. Archaeological Prospection)

## Slide 26: Trend removal (LRM)
-1 m
1 m
50 m Gaussian trend removal
0
100 m
270 m
280 m

## Slide 27: Trend removal (LRM)
can be used as input to other methods
works extremely well with gentle slopes
level of smoothing
introduces artefacts (e.g. artificial banks and ditches)

## Slide 28: Slope gradient
the first derivative of a DEM
inverted greyscale retains relief representation
Doneus et al. 2006. BAR International Series.
5

## Slide 29: Slope gradient
0°
90°
0
50 m

## Slide 30: Slope gradient
easy to compute and interpret
included in standard GIS software
works well in combination with hill-shading
works well on most types of terrain
retains saturated areas
additional information needed for interpretation

## Slide 31: Sky View Factor
determines the size of the visible sky
elevation angle is determined into multiple directions and to the given distance
considers a hemisphere only
values between 0 and 1
Kokalj et al. 2011. Antiquity.
6

## Slide 32: Sky View Factor

## Slide 33: Sky View Factor
0
1
0
50 m
16 10 m (20 px)

## Slide 34
0
50 m
16 10 m (20 px)
Sky View Factor
1
0.6

## Slide 35: SVF – Noisy data
Lidar Data Copyright
State Office for Cultural Heritage Baden-Wurttemberg
0
100 m
16 10 m (10 px)

## Slide 36: Anisotropic SVF
0
100 m
16 10 m (20 px)
1
0.8
Lidar Data Copyright
Janus Pannonius Archaeology Museu

## Slide 37: Sky View Factor
no saturations
clear distinction between protruding features and depressions
particularly useful for complex features
helps with noisy data
intuitive
“washout effect” on very flat terrain with very low protruding features

## Slide 38: Openness
quantifies the degree of unobstructedness of a location
very similar to SVF
positive and negative
Doneus 2013. Remote Sensing.
7

## Slide 39: Comparison SVF - Openness
SVF
positive openness
negative openness

## Slide 40: Comparison SVF - Openness
SVF
positive openness

## Slide 41: Openness – positive
50
95°
0
50 m
16 10 m (20 px)

## Slide 42: Openness – negative
50
95°
0
50 m
16 10 m (20 px)

## Slide 43: Openness
no saturations
enhances concavities and convexities
useful for complex features
completely removes general topography
useful for automatic detection
the same value on different slopes
negative openness not very intuitive to interpret

## Slide 44: Solar insolation
amount of the solar energy received at the surface
direct, diffuse and global solar insolation
Challis et al. 2011. Archaeological Prospection.
8

## Slide 45: Diffuse solar insolation

## Slide 46: Global solar insolation

## Slide 47: Solar insolation
preserves a sense of general topography
suitability of land for human activities
complex and time consuming calculations
numerous options can confuse the user
“washout effect” on very flat terrain

## Slide 48: There‘s more?!!!
Planimetric and profile curvature
Contextual filtering
  edge detection (Laplacian, Sobel’s, Rober’s, Prewitt, Frei and Chen…)…
Lambertian relief shading
Multidirectional oblique-weighted (MDOW) shaded relief
Cumulative visibilty
Local dominance
Accessibility (Miller 1994)
Multi Scale Integral Invariant (Mara 2012)
…

## Slide 49: Multi Scale Integral Invariant
0
50 m
8

## Slide 50: What to use?

## Slide 51: What to use?
depends on:
  data collection and processing
  terrain
  features
  …

## Slide 52: A solution?
a combinaton of hillshade, slope severity and SVF
9

## Slide 53: Recording… what?

## Slide 54: Visualizations for scientific publications
because several factor have a big influence on how features are displayed it is imperative to include at least the following into the description of an image:
  visualization method
  colour legend
  data range
  data stretch type

## Slide 55: Some help
  http:\\iaps.zrc-sazu.si/en/svf
  Relief Visualization Toolbox standalone and IDL code
  http://sourceforge.net/projects/livt/
  Lidar Visualisation Toolbox standalone

## Slide 56: References
Kokalj, Ž., Oštir, K., Zakšek, K. 2011. Application of sky-view factor for the visualization of historic landscape features in lidar-derived relief models. Antiquity 85, 327: 263-273.
Kokalj, Ž., Zakšek, K., Oštir, K. 2013. Visualizations of lidar derived relief models. In: Opitz, R., Cowley., D. (eds) Interpreting archaeological topography – airborne laser scanning, aerial photographs and ground observation. Pp. 100-114.
Štular, B., Kokalj, Ž., Oštir, K., Nuniger, L. 2012. Visualization of lidar-derived relief models for detection of archaeological features. Journal of Archaeological Science 39: 3354-3360.
Yoëli, P. 1965. Analytische Schattierung. Ein kartographischer Entwurf. Kartographische Nachrichten 15: 141-148.
Devereux, B.J., Amable, G.S., Crow, P. 2008. Visualisation of LiDAR terrain models for archaeological feature detection. Antiquity 82, 316: 470-479.
Challis, K. 2006. Airborne laser altimetry in alluviated landscapes. Archaeological Prospection 13, 2: 103-127.
Challis, K., Kokalj, Ž., Kincey, M., Moscrop, D., Howard, A.J. 2008. Airborne lidar and historic environment records. Antiquity 82, 318: 1055-1064.
Hesse R. 2010. LiDAR-derived Local Relief Models - a new tool for archaeological prospection. Archaeological Prospection 17, 2: 67-72.
Doneus, M., Briese, Ch. 2006. Full-waveform airborne laser scanning as a tool for archaeological reconnaissance. In: "From Space To Place. Proceedings of The 2nd International Conference On Remote Sensing In Archaeology", Bar International Series, 1568 (2006), 99 - 105, December 2006.
Doneus, M. 2013. Openness as visualization technique for interpretative mapping of airborne LiDAR derived digital terrain models. Remote Sensing 5: 6427-6442.

## Slide 57
Thank you for your attention!
ziga.kokalj@zrc-sazu.si
  http:\\iaps.zrc-sazu.si/en/rvt